## Slide 1: Analytical Tools for Process Analysis and Improvement
BUSI 104 Operations Management
Professor Arnheiter

## Slide 2: What is Cycle Time (CT)?
Actual amount of time needed to complete given task and move it along to next production step.
Time between completion of two discrete successive units (or lots) of production.
Can be defined for entire process, or portions of process, e.g., CTProcess, CTDrilling, CTDepartment

## Slide 3: Lead Times
Total Lead time or Order-to-delivery time (OTD); Total time customer must wait to receive product or service after placing order.
Lead time (LT). Time job spends as work-in-process (WIP). Includes non-value added time.

## Slide 4: Throughput (TH)
Average quantity of good (non-defective) items produced by process (machine, workstation, line, office, etc.) per unit time.
Upper limit on throughput is capacity – e.g., what is the maximum number of units we can ship per hour?
e.g., How many cartons are we shipping per hour (a rate measurement)?
TH = 1/CT

## Slide 5: Capacity
Measure of how much can be produced or serviced in specified period of time.
Capacity Utilization is a Measure of how much output was actually achieved relative to capacity.
e.g., Our maximum output is six boxes/day
1
2
3
4
5
6

## Slide 6: Other Important Terms
Bottleneck - Factor which limits production. Usually task with longest CT is process bottleneck.
Bottlenecks can be: Specific workers
Specific machines
Specific tasks
Idle Time - Time in which useful work is not being performed.
Idle time can be associated with Workers or Equipment!

## Slide 7: Little’s Law
Where:
LT = Lead Time
CT = Cycle time (1/TH)
WIP = Work in process
TH = Throughput (e.g., customers/hour)
LT = CT x WIP = WIP/TH
It may be Little, but it’s the Law!

## Slide 8: Examples of Little’s Law
Assume WIP = 6 customers, CT = 2 min/unit
F
E
D
C
B
1
2
4
3
5
6
Time = 2
A
F
E
D
C
1
2
4
3
5
6
Time = 4
B
A
F
E
D
C
B
A
1
2
4
3
5
6
Time = 0
Idle

## Slide 9: Little’s Law (continued)
F
E
D
1
2
4
3
5
6
Time = 6
B
A
C
F
E
1
2
4
3
5
6
Time = 8
B
A
C
D
F
1
2
4
3
5
6
Time = 10
B
A
C
D
E
1
2
4
3
5
6
A
F
B
Time = 12
C
D
E
For Customer F, what was the expected lead time?

## Slide 10: Cycle Time Example 1
Task A
Task B
CTA = 5 minutes
CTB = 2 minutes
Finished Goods Inventory (FGI)
CTbottleneck =
Capacity =
Idle Time at B =

## Slide 11: Cycle Time Example 2: Add Second Worker at Task A
Task B
CTA = 5 minutes
CTB = 2 minutes
FGI
Task A
CTA = 5 minutes
Task A
CTbottleneck =
Capacity =
Idle Time at B =

## Slide 12: Example 3: Add 3rd Worker
Task B
Task A
CTA = 5 min
Task A
CTA = 5 min
Task A
CTA = 5 min
CTB = 2 min
FGI
Idle Time =
CTbot =
Capacity =

## Slide 13: Two More Important Metrics
To = Raw process time (average time for a single job to traverse an empty line)
Critical WIP level = W0 = (THbottleneck)(T0)

## Slide 14
Critical WIP
Unbalanced lines, W0 < number of machines.
CT = 2 min
CT = 3.5 min
CT = 2 min
CT = 2 min
Balanced lines, W0 = number of machines (i.e., one job at each machine)
At critical WIP level (W0), line achieves maximum TH with minimum LT (i.e., T0).

## Slide 15
Critical WIP Example
CT = 6 min
CT = 10 min
CT = 8 min
W0 =

## Slide 16: Batch Size Concepts
?
What is batch size in this situation?
Make one unit then move to next operation
Dedicated machine

## Slide 17: Process Batch Size vs. Transfer Batch Size
Process Batch Size = 50
Transfer Batch Size = 50
50 Model X
50 Model Y
Change-over
50 Model X
50 Model X
Move
Move

## Slide 18
Incorporating Changeover (C/O) Time Into Cycle Time
CT =
Internal C/O Time
Item Run Time
X
+
Process Batch Size

## Slide 19
FGI
R/T = 5 minutes/sandwich
C/O = 15 minutes
R/T = 2 minutes/sandwich
C/O = 3 minutes
Example: C/O and Batch Sizes
All items in batch are processed before moving to next person.
Assume WIP = 3 batches.

## Slide 20
For 10 sandwiches/batch, what is system CT and LT? What is the daily capacity (assuming two, 480-minute shifts)?
For 20 sandwiches/batch, what is system CT, LT and capacity?
Example: C/O and Batch Sizes

## Slide 21: Solutions - C/O and Batch Sizes
For Batch size of 10:
For batch size of 20:

## Slide 22: Process Gantt Charts Schedule I
Task 1
CT = 6 min/unit
Task 2
CT = 10 min/unit
Task 3
CT = 8 min/unit
Job 1
Task 1
Task 2
Task 3
Job 2
Job 3
Job 1
Job 2
Job 3
Job 1
Job 2
Job 3
6
Time =
10
16
20
26
36
24
34
44
One Feasible Production Schedule
Inserted Idle Time Keeps WIP at W0

## Slide 23: Process Gantt Charts Schedule II
Task 1
CT = 6 min/unit
Task 2
CT = 10 min/unit
Task 3
CT = 8 min/unit
Job 1
Task 1
Task 2
Task 3
Job 2
Job 3
Job 1
Job 2
Job 3
Job 2
6
Time =
12
18
24
16
Jobs Pushed Back-to-Back Into Task 1
WIP Builds Up in System and LT Increases*
Job 4
Job 5
Job 6
Job 1
Job 4
Job 3
30
36
24
26
34
36
44
46

## Slide 24: Process Gantt Charts Schedule III
Task 1
CT = 6 min/unit
Task 2
CT = 10 min/unit
Task 3
CT = 8 min/unit
Job 1
Task 1
Task 2
Task 3
Job 2
Job 3
Job 1
Job 2
Job 3
Job 1
Job 2
Job 3
6
Time =
10
16
20
26
28
30
38
Equipment-Paced Flow Line
Each Job Moves to Next Task Every (CTProcess) minutes
40
48
50
Job 3 ready at time t = 50

## Slide 25: Direct Labor Concepts
Direct labor content - Actual amount of work contained in each unit of product, including changeover.
Direct labor cost - Refers to actual wages paid. Idle time adds to direct labor costs, but does not affect labor content.

## Slide 26: Direct Labor Utilization
Direct Labor Utilization = Direct Labor Content
Total Available Labor Time
Total available labor = direct labor content + idle time

## Slide 27
Direct Labor Calculations
What is the direct labor content in Example 1 (the job shop with Task A CT = 5 min, and Task B = 2 min, as shown earlier)?
What is the direct labor cost for example 1?
What is the direct labor content for the split process shown in example 2?
What is the direct labor cost for example 2?

## Slide 28: Direct Labor Example Solutions

## Slide 29: Paced Assembly Lines
Parts move through zones containing one or more operators.
Operators usually able to complete their task(s) while part is in their zone.
Capacity increments usually much smaller than in batch flow operation.
Tasks assigned to workers can usually be split into fine increments.

## Slide 30: Machine-Paced Assembly Line for Laptop Computers
1
2
3
4
5
6
7
8
9
10
White stripes on belt are 1.2 meter apart
Software loading – no operator required
Ten Operator Stations
One unit is finished every 120 seconds
Belt is 14.4 meter long
CT= 110 s
114 s
101 s
107 s
103 s
107 s
108 s
93 s
102 s
105 s
208 s
Tasks at Station 9 include: (1) Insert USB device and initiate operating system and software installation process, and (2) Test touch pad.

## Slide 31: Questions for Laptop Computer Assembly Line
If line is currently running at CT = 120 sec/unit, is it possible to run this line at a faster pace?
Assuming the line is machine-paced, what is T0? If the line were operator paced, what would T0 be?
What is the line speed (meter/minute)?
What is the LT? Assume WIP is a constant 12 units.
Assuming one 7.5 hr shift, what is the line capacity?
What are the direct labor content and direct labor costs?
What is the direct labor utilization rate?

## Slide 32: Solutions to Computer Assembly Line Exercise

## Slide 33: Solutions to Computer Assembly Line Exercise

## Slide 34: Practice Problem Three Workers in Series
Worker A
Worker B
Worker C
Run time = 2 min/unit
C/O = 13 min
Run time = 3 min/unit
C/O = 7 min
Run time = 3 min/unit
C/O = 6 min
For differing process batch sizes (1, 10, 30), answer the following:
Expected cycle time of the department
Raw processing time
Critical WIP level of the department
Expected LT when WIP =10 batches
Daily capacity, assuming two, 480-minute shifts

## Slide 35: Worksheet for Series System Exercise
Question | Process batch size = 1 | Process batch size = 10 | Process batch size = 30
Expected cycle time of the department (CTbot) |  |  | 
Raw processing time |  |  | 
Critical WIP level of the department |  |  | 
Expected LT when WIP = 10 batches |  |  | 
Daily capacity assuming two, 480-minute shifts Batches/day = Pieces/day = |  |  | 

## Slide 36: Calculating Theoretical Minimum Number of Workstations and Efficiency
In order to meet holiday demand, Penny’s Pie Shop requires a production line that is capable of producing 90 pecan pies per week, while operating only 40 hours per week. There are only 4 steps required to produce a single pecan pie with respective cycle times of 4 minutes, 4 minutes, 28 minutes, and 9 minutes.
What should be the line’s cycle time (CT)?

## Slide 37: Example - Continued
What is the smallest number of workstations Penny could hope for in designing the line considering this cycle time?
Suppose that Penny finds a solution that requires 4 stations. What would be the efficiency of this line?