## Slide 1: Supply Chain Integration Supplier selection, information exchange (RFID and VMI), intermodal shipping methods, reverse logistics, green supply chains, e-waste.
BUSI 104 – Operations Management
Professor Ed Arnheiter

## Slide 2: Rating Suppliers Using a Cost of Quality Approach
Quality Cost Performance Index = QCPI =
Supplier Quality Cost + Purchased Cost
Purchased Cost
Typical Supplier Quality Cost include items such as:
  Cost of processing incoming rejections
  Cost of complaint investigations
  Cost of Processing in Receiving Inspection
  Cost of a Defective Product after Receiving Inspection
There are many other, possibly relevant, costs. This is not an exhaustive list of supplier quality costs!

## Slide 3: Supplier Rating Example Total Number of Items Purchased from Suppliers During October
Supplier | Number of Items Purchased
A | 55,500
B | 22,440
C | 33,700
D | 60,800
E | 33,300

## Slide 4: Supplier Rating Example Data for October
 | A. Processing Incoming Shipments |  | B. Complaint Investigations | 
Supplier | No. of Rejected Shipments | Cost to document & return a shipment to supplier | Total Investigation time required by Analyst (Hr) | Average Analyst Wage ($/hour, fully burdened)
A | 2 | $ 100 | 10 | $ 50
B | 3 | $ 125 | 12 | $ 50
C | 4 | $ 100 | 9 | $ 50
D | 1 | $ 220 | 9 | $ 50
E | 2 | $ 130 | 15 | $ 50

## Slide 5: Supplier Rating Example (cont.) Additional Data for October
  * A study indicated that no matter which action was taken on the defective item (rework, scrap, sorting, RTV, etc.), the purchased cost of that item provided a reasonable estimate of the quality costs incurred. Verify whether such an approach is reasonable under your specific circumstances!
 | C. Receiving Audit Processing |  |  | D. Cost of a Defective Item after Receiving Audit | 
Supplier | Labor Standard (Hours/ shipment) | Average Auditor Wage ($/hour, fully burdened) | Number of Shipments processed | Number of defective Items found AFTER receiving audit | Initial purchase price of each Item*
A | 1.20 | $ 25 | 50 | 98 | $ 1.80
B | 1.40 | $ 25 | 42 | 43 | $ 2.05
C | 1.60 | $ 25 | 46 | 4 | $ 1.72
D | 1.00 | $ 25 | 17 | 56 | $ 3.75
E | 1.60 | $ 25 | 46 | 15 | $ 0.78

## Slide 6: Supplier Rating Exercise (cont.)
Complete the entries in the Excel file Cost of Quality Supplier Rating Exercise and calculate the QCPI for each supplier.
Which supplier has the best quality performance index (QCPI)?
Based on the assessment scale shown below, rate each of the five suppliers.
QCPI | Supplier Rating
1.000-1.009 | Excellent
1.010-1.039 | Good
1.040-1.069 | Fair
1.070-1.099 | Poor
1.100+ | Immediate C/A required
What are some of the options for dealing with the poorly performing supplier(s)?

## Slide 7: Information Exchange: Inventory Tracking Technology

## Slide 8: RFID Technology Hurdles
First generation RFID technology had problems with variety of materials, including liquids and metals.
Early RFID readers only had 33 percent accuracy rate.

## Slide 9: Common RFID System

## Slide 10: Information Exchange: Vendor Managed Inventory (VMI)
Supplier specifies delivery quantities sent to customers through distribution channel using electronic data
VMI, JIT Distribution (JITD), and Efficient Consumer Response (ECR) refer to similar concepts, different industries.
  Grocery & apparel: ECR
  Automobile: VMI and JITD
Notes: http://www.endries.com/eport/images/bin_scanning.jpg

## Slide 11: Some Features of VMI
Shortens supply chain
Centralizes forecasting
Frequent communication; inventory, stock-outs, planned promotions
Trucks filled in prioritized order - Items expected to stock out have top priority, etc.
Notes: http://www.atlanticfasteners.com/images/Atlantic-Fasteners-point.jpg

## Slide 12: Variety of Applications
Food & Beverage Vending Machines
Tools and Tooling Vending Machines
In-Store Shelf Space Management

## Slide 13: Tips for Successful VMI Program
Address distributor skepticism
Introduce system in distributor-owned warehouses on pilot basis.
Engage neutral consultant in meetings among vendor, distributor, & sales force
Simulate system off-line before implementing
Don't exaggerate benefits!

## Slide 14: Multimodal Shipping Solutions
Notes: Exploit strengths of multiple transportation modes through physical, information, and monetary flows that are as seamless as possible.
Shipping containers have become more standardized, and information systems for tracking shipments more accurate.

## Slide 15: Example of Multimodal Solutions
Standardized containers can be quickly moved to rail cars or truck beds

## Slide 16: Reverse Logistics
Activities involved in managing, processing, reducing and disposing of hazardous or non-hazardous waste from production, packaging and use of products, including reverse distribution processes.
Also includes product recalls, recycling, and refurbishing

## Slide 17: Flow of Goods in Forward & Reverse Logistics
Supplier
Manufacturer
Retailer
Customer
Landfill
Waste
Processor
Collector
Forward Logistics
Reverse Logistics

## Slide 18: Retail Returns Management Reverse Logistics Challenge

## Slide 19: Environmental Problems: Need for a “Closed-Loop Economy”
Population Growth
Increasing Consumption needs
Finiteness of Resources
Scarcity of Disposal Capacities
Contradiction of Needs and Supplies of Natural Resources and Capacities

## Slide 20: Hierarchy of Waste Treatment Activities
Reuse
Remanufacturing
Recycling
Disposal with Energy Recovered
Disposal in Landfill
Dyckhoff, H., R. Lackes, and J. Reese, Supply Chain Management and Reverse Logistics, Springer, 2004, p. 165.

## Slide 21: Example of Reverse-Flow Logistics
Supplier
Manufacturing
Warehousing
Reverse
Flow
Delivery
Reuse
Refurbish
Recycle
Copacino, W.C., Supply Chain Management: The Basics and Beyond, St.Lucie Press/APICS, 1997, p.185.

## Slide 22: Reverse Logistics: E-Waste Problem!!
A Mountain of Waste

## Slide 23: E-Waste Global Volumes 1 Metric Ton = 1.102 U.S. Ton 1 kg = 2.2 pounds
http://www.wastedive.com/news/us-produces-most-per-capita-e-waste-worldwide/266465/

## Slide 24: e-Waste Recycling Plant Roseville, CA Built by, and formerly(?) operated by, Hewlett Packard (HP)

## Slide 25: E-Waste E-waste is mined for lead, gold, copper and other metals
Heating computer board to remove computer chips
One of the world’s dirtiest jobs – e-waste disposal