## Slide 1: Visual tools for process analysis and improvement Pareto charts, histograms, run charts, scatter diagrams, etc.
BUSI 104 – Operations Management
Professor Ed Arnheiter

## Slide 2: Common Tools of Process Analysis and Improvement
Process Flow Diagrams (broadly defined, this can be tabular as well)
Cause & Effect diagrams (fishbone diagrams)
Run Charts
Histograms
Checklists (a data collection technique)
Pareto Charts
Scatter Diagrams

## Slide 3: Using OM Explorer to Create Process Charts
OM Explorer>Solvers>Process Analysis>Process Charts

## Slide 4: Process Chart in Tabular Form

## Slide 5: Cause-and-effect Diagrams
Visual brainstorming tool used to isolate ONE specific defect, problem, or undesirable condition and determine potential causes.
Categorization helps identify causes and link common causes that can be addressed by similar solutions.
After developing diagram, classify variables as Constant, Noise, or Experimental.
________
________
Problem or
Defect
Methodology
Materials
Machinery
Manpower
Measurement
Mother Nature
________
________
________
________
________
________
________
________
________
________
________
________
________
________
________
________
C = Constant: This task is currently controlled with an SOP
N = Noise: This task currently is not controlled. Control it with an SOP if possible. Leave it as an N if necessary.
X = Experimental: I am experimenting with this task

## Slide 6: Cause-and-effect Diagram Example

## Slide 7: Run Chart Features
Vertical axis shows numerical value of output
Data points plotted in sequential order
Points are connected by a line to aid in visual interpretation
Chart: Time
 | 16 | 13 | 22 | 12 | 13 | 22 | 13 | 19 | 21 | 12 | 31 | 12 | 12 | 21 | 14 | 25 | 16 | 15 | 34 | 12 | 25 | 15 | 18 | 33 | 22 | 19 | 14 | 15 | 14 | 19 | 31 | 18 | 19 | 17 | 21

## Slide 8: Histograms

## Slide 9: Pareto Principle
80% of the effects can be traced to 20% of the causes (the “vital few”)
Named after Vilfredo Pareto, an Italian economist, who observed that vast majority of wealth was in the possession of only a few people

## Slide 10: Pareto Charts
Bar height shows relative importance, in
descending order
Bars represent each stratified category
Chart: Pareto Chart of Errors by Dept
| d | m | f | l | b | g | n | i | Other
 | 6789 | 2365 | 987 | 797 | 657 | 476 | 476 | 465 | 1220
 | 0.47702 | 0.6432 | 0.71255 | 0.76855 | 0.81471 | 0.84816 | 0.8816 | 0.91428 | 1
Vertical axis shows percentages
“Other” category combines stragglers
Vertical axis shows count of data points
Red line shows cumulative percentages
Visual depiction of Pareto principle
Useful for drilling down into root causes.

## Slide 11: Scatter Diagrams
Positive correlation
  An increase in X is likely to be associated with an increase in Y
No correlation
  The Y response is likely to be dependent on some other variable
Negative correlation
  An increase in X is likely to be associated with a decrease in Y
Y
X
Y
X
Y
X
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 12: Scatter Diagram for Customer Satisfaction
Customer Satisfaction
Time Spent in Queue (minutes)
0
5.0
10.0
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 13: Using OM Explorer to Create Bar, Pareto and Run Charts
OM Explorer>Solvers>Process Analysis>Bar. Pareto and Line Charts

## Slide 14: OM Explorer Results