## Slide 1: Lean Management Philosophy, tools and techniques, Kaizen, value stream mapping, lean services.
BUSI 104 – Operations Management
Professor Ed Arnheiter

## Slide 2
Lean can be defined as a business system that seeks to maximize value to customers, both internal and external, while simultaneously removing wasteful activities and practices.
Lean Pioneers
W. Edwards Deming
Henry Ford
Taiichi Ohno
Creator of the Toyota Production System (TPS)

## Slide 3
Henry Ford & the automobile industry
  Moving assembly line
  Model T reduced in price from $850 to $290
Ford (in 1926) claimed that the “lead time from the mining of iron ore to the production of an automobile was 81 hours.”
The Original “Lean Thinker”

## Slide 4: Human Aspects of Lean
Fear-free environment
Respect for People!
Blameless culture
Training
Discipline
Bottom-round management

## Slide 5
A Recurrent Theme of Lean Management
Continuously strive to:
  Minimize all forms of waste in the value-stream.
  Eliminate non value-added activities.
Notes: Ended here on 3/24/16

## Slide 6
Applying Lean in Manufacturing
Specify value - from each customer’s perspective
Map value stream – understand all activities that take place while manufacturing the product
Optimize flow - minimize interruptions that could take place during production
Create pull – work should be initiated by customer demand
Strive for perfection – goal is zero waste

## Slide 7
Applying Lean in Services
Specify value - from each customer’s perspective, considering all "dimensions" of quality
Map service process – understand all activities that take place while providing service
Identify value-added activities and waste - focus on main areas of waste supplemented with data
Work to eliminate waste and add value – attempt to simplify rather than complicate
Continuously evaluate the service – goal is maximal value with minimal waste

## Slide 8: More Key Lean Traits
Strong Supplier Relationships
Robots for Dangerous or Unpleasant Tasks

## Slide 9: Value Added vs. Non-value Added
Value Added (VA)
  Activities which change form, fit, or function of product/service AND
  Activities which customer cares about/is willing to pay for AND
  Activities done right the first time
Non-Value Added
  Activities that consume resources but create no value in the eyes of the customer
  Necessary Non-Value Added (NNVA)
    Activities which may be necessary for business or other reasons but do not add value in the eyes of the customer
    May include activities required for the process to function, regulatory, compliance, legal, etc.
    Waste
    Pure waste (8 forms of waste)

## Slide 10
Waste
      Required Non-Value-Add (NVA) Activity
VA Activity - Something Changes, Done Right, Customer Cares
Remember: DOWNTIME
DEFECTS
OVER PRODUCTION
WAITING
NOT USING PEOPLE Well
TRANSPORTATION
INVENTORY
MOTION
EXCESS PROCESSING
The Eight Wastes

## Slide 11: Defects (Toyota calls “Rework”)
Errors, mistakes, rework – can be very costly

## Slide 12: Overproduction (Toyota calls Over Processing)
Producing more than required, earlier than required or faster than required

## Slide 13: Waiting
Employees and customers waiting for resources to perform their work

## Slide 14: Not Using People Well

## Slide 15: Transportation (Toyota calls this Conveyance)
Excessive product or data movement
Diagram of backhoe travel

## Slide 16: Inventory
Holding more inventory (materials and information) than required
Inventories add clutter and take up space.
Usually symptom of unreliable supply chain.
WIP is direct result of overproduction and waiting

## Slide 17: Motion
Excessive motion of people

## Slide 18: Excess Processing (Toyota calls Over Processing)
Doing more work than is really necessary
Using expensive equipment when simpler machines would suffice

## Slide 19
Flow
Use small batches or single-piece flow
Assembling Model T clutch plates
Use continuous flow wherever possible

## Slide 20
Single-Piece Flow in Services
Some services (with fairly constant processing times) can achieve single "customer" flow
  example: an Optometrist office
Many services (with highly variable processing times) should not consider single "customer" flow
  example: IT troubleshooting

## Slide 21
Pull
Use where continuous flow is interrupted and upstream process still operates in batch mode
A
B
C
D
E
F
In
Out
Continuous Flow
Supermarket
Schedules forging process
Upstream Department
(Batch Mode)
Don’t make anything until needed by downstream customer.

## Slide 22: Visual Workplace
Anyone should know the who, what, when, where, why and how of a work area within five minutes
…without having to ask anyone
…without having to search
…without having to analyze
…without having to interpret
…without having to…..
Source: Productivity, Inc.

## Slide 23: Visual Workplace
Situation
  What are our goals and targets? How are we doing in meeting them?
  Are conditions abnormal, or hazardous?
  How is the operation proceeding?
Location
  Where can I find _____?
  Where does this item go?
  What goes here?
  What caution/restrictions apply in this area?
Action
  What needs to be done?
  Am I doing this properly?
  Where does this go next?
  What is the next item to be worked on?
People
  Who does what around here?
  Who can help me?

## Slide 24: Situation – How do we Know?
Before
Before
After
After

## Slide 25: Situation – How do we Know?
Top: number expected at this time if we are to meet target.
Bottom: actual production completed at this time.
In some Lean systems, an "andon" is visual mechanism to signal that work will not be completed within takt time allocation.

## Slide 26: Location – Where can I Find ____?

## Slide 27: Location – Where can I Find ____?

## Slide 28: Action – What needs to be done?
Sample product, and graphical work aids for how each terminal should look

## Slide 29: People – Who does what?

## Slide 30
The 5S’s Support the Visual Workplace
“Sort”
  Sort through, then sort out
  Identify what you need, and discard what is unnecessary.
“Straighten”
  Organize what remains.
  Assign separate location for essential items.
  Make space self-explanatory (obvious where items belong)

## Slide 31
The 5S’s (Continued)
“Shine”
  Clean equipment, tools, and workplace.
  Keep workplace spotless at all times.
“Standardize”
  Schedule cleaning & regular maintenance for equipment and tools.
“Sustain”
  Stick to rules - make them way of life.

## Slide 32
Before
After
5S Example
Which 5S Element is obvious from the RH Photo?

## Slide 33
5S Examples

## Slide 34
Work Areas Needing 5S Audit!
Versus

## Slide 35
Mistake Proofing (Poka-Yoke)
Descending degree of difficulty:
Develop processes that cannot make defects
Develop sensing within process to shut down when defect has been made
If defect made, system does not allow part to go to next operation.

## Slide 36: Is it a Mistake Proofing Device?
Does it prevent the mistake or detect the defect?
Is it 100% reliable?
Is it easy to implement and to use?
Is it durable and easy to maintain?
Is it low cost?
Self-checking of product thickness

## Slide 37: Mistake Proofing Example
Press both buttons simultaneously to activate machine

## Slide 38
Everyday Examples

## Slide 39
Everyday Examples

## Slide 40
Takt Time
Takt time is calculated value that sets pace of production to match rate of customer demand.
Ideally, we make 100/minute only if customer demand is 100/minute

## Slide 41
Takt Time Calculation
Forecast demand rate
Set throughput equal to demand rate
Calculate takt time (example follows

## Slide 42
Example Takt Time Calculation
Available work time per shift
Customer demand rate per shift
Shift time = 8 hours = 28,800 seconds
Breaks = 20 minutes = -1200 seconds
Total daily operating time = 27,600 seconds
Total daily required quantity = 690 pieces per shift
Takt Time = 27,600/690 = 40 seconds

## Slide 43
Takt Time in Services
Some services operate like manufacturing processes relative to their near-constant processing times:
  Bill processing, routine personal services
But in most cases, takt time cannot be applied to services since service times often vary significantly from customer to customer:
  Help lines, proposal development, repair, engineering design, negotiations, etc.

## Slide 44
Related Technique: Andon
In some Lean systems, an "andon" is visual mechanism to signal that work will not be completed within takt time allocation.
  Examples: defect, shortage, machine malfunction, incomplete information to proceed.
  Example signals: cord, light, andon boards or post-it note.
Notes: The andon board communicates abnormalities along the assembly line.
Ended here on 3/31/16

## Slide 45
Value Stream Mapping
A Special Type of Process Flow Diagram

## Slide 46
One-page, data rich, picture of macro level processes in an organization.
Tool used to analyze the non valued-added time of the entire process.
Tool used for identification of opportunities for improvement
Current state value stream maps identify the improvement opportunities
Future state value stream maps demonstrate the “should be” future state
The Value Stream Map (VSM)

## Slide 47
The Value Stream Perspective
Total Value Stream
Suppliers
Your Plant or Company
Customer to End User
“Local” optimization
“Global” optimization

## Slide 48
VSM Uses Set of Special Icons
Different from Traditional PF Diagrams

## Slide 49
VSM Uses Set of Special Icons
Different from Traditional PF Diagrams

## Slide 50
Acme Stamping Current State Timeline Added
Stamping
200 Ton
1
Weld #1
1
Weld #2
1
Assy #1
1
Assy #2
1
Shipping
Staging
CT = 1 s
CO = 1h
U/T = 85%
27,600 s avail.
CT = 39 s
CO=10 m
U/T= 100%
27,600 s avail.
2 Shifts
CT = 46 s
CO=10 m
U/T= 100%
2 Shifts
27,600 s avail.
CT = 62 s
CO = 0
U/T = 100%
2 Shifts
27,600 s avail.
CT = 40 s
CO = 0
U/T = 100%
2 Shifts
27,600 s avail.
I
Coils
5 d
7,000
1,700
2,450
1,840
4,140
500 ft coils
Michigan
Steel
State St
Assembly
Tray = 20 pc
2 Shifts
18,400 pc/mo
-12,000 “L”
-6,400 “R”
Tue & Thu
1x
daily
Prod Cont
Daily Ship
Schedule
Weekly Schedule
MRP
Weekly
fax
Daily order
6wk
forecast
90/60/30
forecasts
I
I
I
I
I
1 s
39 s
46 s
62 s
30 s
5 d
9.89 d
2.83 d
5.50 d
2.67 d
4.5 d
30.4 days
218 sec
40 s

## Slide 51: Productive Ratio Calculations
Productive Ratio = (218/838,900)(100)% = 0.026%

## Slide 52: Example VSM Timeline Calculations
Step 1
1
9.04 s
12.35 s
14.8 s
8.5 s
45 s
2025 s
I
Step 2
1
Step 3
1
Step 4
1
Step 5
1
I
I
I
CT = 9.04 s
CT = 12.35 s
CT = 14.8 s
CT = 8.5 s
40
5
20
45
Productive ratio =
FPY = 97.2%
FPY = 96.8%
FPY = 96.3%
FPY = 98.3%
FPY = 100%
Rolled Throughput yield (RTY) =
% Correct & Accurate (%CA) as seen by the customer

## Slide 53
Acme Stamping: Completed Future State

## Slide 54
Current State Map for Blood Bank

## Slide 55
Current State – Healthcare Example